main data structure:
WSPRbeaconContext	(callsign, locator)
->TxChannelContext *_pTX; (also _pbyte_buffer[256] and dial freq)
-> PioDco RfGenStruct *_p_oscillator {i think only this needed for core oscillator)
-> PIO _pio; (the actuall PIO instance)
->GPStimeContext *_pGPStime; (buffer for parsing GPS..)
-> GPStimeData _time_data; (lat/lon, _i32_freq_shift_ppb..)
->WSPRbeaconSchedule _txSched (not much, originally had simple slot info)
**********************************************
TxChannel.c,
->an ISR (triggerd each WSPR bit cycle) calls PioDCOSetFreq based on dial-freq, modulated with WSPR step-size (~3Hz), and drift correction (_i32_freq_shift_ppb) via PioDCOGetFreqShiftMilliHertz in piodco.c
***************************************************************
this all went away from kazu I think:
Main.c uses multicore_launch_core1 (from SDK) to launch Core1Entry (a routine in core1.c)
core1.c
->Core1Entry calls PioDCOInit piodco.c to load the dco2.pio assembly language file into the 0th PIO (the Cmake file lists the actual	dco2.pio filename, inside that file meta data gives it a logical name by which t is invoked)
->Core1Entry uses the PioDco struct to call loop PioDCOWorker2 (in /piodco.c, as RAM)
piodco.c
->loops PioDCOWorker2
-- uses pio_sm_put_blocking (SDK) to shovel loop_count to state machine
>PioDCOSetFreq sets si32precise_cycles to a (<<24 scaled up) value of required loops, based on clock speed and required frequ
*******************************************
si32precise_cycles= the exact theoretical number of cycle to loop, scaled by 2^24 ) (if directly unscaled its non-integer)
i32wc= the actual number of extra operations per pulse period in the assembly language loop
i32acc_error= the number of cycles (scaled by 2^24) that were dropped/added on last go. these will get added to the next try.
*********************
GPStime.c
-Still sets an IRQ for serial incoming data (GPStimeUartRxIsr)
->GPStimeInit loads my timer_PIO.pio assembly language file into the 2nd PIO (referenced in MakeFile pico_generate_pio_header(pico-WSPRer ${CMAKE_CURRENT_LIST_DIR}/hf-oscillator/gpstime/timer_PIO.pio))
->Ram based GPStimePPScallback (ISR of the PPS input pin) reads timing value from timer-PIO.pio to create _i32_freq_shift_ppb (frequ correction of onboard xtal)
*****************************
dco2.pio (was used by Pikashin method)
- takes a minimum of 8 instructions per output pulse. That is why maximum output frequency is 1/8 of